## Slide 1
Georgia Brownfield Association
2025 Seminar
Gas Station Remediation and Redevelopment
in Historic South Atlanta
April 16, 2025

## Slide 2: The City of Atlanta Brownfield Program is funded with EPA grants
Assessment Grants: provide funding environmental assessments, community engagement, brownfield inventories and cleanup plans.
South Atlanta is in the Jonesboro Road Target Area.
Revolving Loan Fund (RLF) Grants: provide funding to capitalize loans and grants that are used to clean up brownfield sites.
City of Atlanta Brownfield Target Areas

## Slide 3: Atlanta/Invest Atlanta BRLF Program
Fund Manager- Invest Atlanta
Loans-
  At least 50% of funds have to be loans
  No maximum loan amount
  Low Interest rate- 2%
  Generate Program Income
Subgrants-
  Up to 50% of funds can be subgrants to non-profits
  Must own property
  $500K maximum subgrant

## Slide 4: Historic South Atlanta- Planning and Zoning
Historic South Atlanta Master Plan adoption - 2018
Create a “Downtown” South Atlanta - retail development should focus on creating a concentrated, walkable destination based on restaurants, the arts, and culture
Rezoning of non-residential areas to Mixed Residential Commercial (including 105 McDonough)- 2019
105 McDonough Blvd:
Lot Consolidation of 4 parcels and Martin Street ROW- 2023
Special Administrative Permit (SAP) of proposed development -2023

## Slide 5: 105 McDonough Phase II ESA Tank Removal- 2019
2017 EPA Assessment Grant
Fuel dispensers, lines and canopy
1,500 gallons of fuel
2 - 4,000 gallon gasoline tanks
1- 2,000 gallon diesel tank
70 cubic yards of contaminated soil
Soil samples 12 ft bgs
UST Closure Report
Restaurant in existing building

## Slide 6: 105 McDonough Phase II ESA- 2023
2020 Assessment Grant
REC-Off-site dry cleaners and two on-site former gas stations
5 soil samples/monitoring wells 24-33 bgs
5 Soil vapor sampling at proposed buildings
Exceedance of VISL residential and non-residential screening criteria
Vapor mitigation measures for structures recommended
PPCAP Amendment to reflect all parcels and Type 2 RRS for proposed mixed use development

## Slide 7: Brownfield Revolving Loan Fund- Subgrant to FCS
Invest Atlanta
Subgrant approval- June 2024
Subgrant increase- January 2025
City of Atlanta/QEP- CHA
Before Remediation- June to October
ABCA
SSQAPP
30-day Community Engagement & meetings
Section 106 Review
FWS/Endangered Species Act review
During and After Remediation
Davis Bacon Compliance
Review/monitoring of remediation
Closeout report

## Slide 8: Other FCS sites- Harolds BBQ ESAs
2020 Assessment: Phase I ESA
Potential REC- adjacent properties A-Tow and automotive uses
UST releases
Phase II ESA- underway
FCS proposes to redevelop the site for neighborhood commercial uses.

## Slide 9: More information about the Brownfield Revolving Loan Fund (BRLF) at:
www.atlantaga.gov/brownfields
Jessica Lavandier- jlavandier@atlantaga.gov
404-450-6442
Thank you!