## Slide 1
Applications of Environmental Forensics AT SITES WITH LEGACY AND EMERGING CONTAMINANTS
APRIL 16, 2025

## Slide 2
Introduction to Environmental Forensics
Large or Small Sites
Many Contaminants
Multiple Legal Frameworks
Identify Parties
Identify financially viable responsible parties (RPs)
Inform Site Investigation Inform site investigation and remediation strategies
Establish Nexus
Develop a defensible factual basis of liability and establish contaminant link
Support Legal Strategy
Inform legal strategy regarding asset purchase or divestiture, cost allocation, liability defense, cost recovery, etc.
Identify Sources
Identify sources of contamination and, where possible, the proportion of contamination contributed by each source

## Slide 3
Multiple Lines of Evidence (LOE) Approach to Forensics
Fingerprinting Analysis
Concentration and Spatial Distribution
Modeling
Contaminant Transport Pathway Analysis
Site History Forensics
Multiple lines
of evidence that
tell a cohesive,
defensible, and compelling story
about the sources
of COCs

## Slide 4
Case Studies
Case Study 2:
Petroleum Age Dating at an Underground Storage Tank Site
Case Study 1:
PFAS Forensics at a Groundwater Site

## Slide 5
Case Study 1:
PFAS Forensics at a Groundwater Site

## Slide 6
Case Study 1 Background
The Case: A former chrome plating facility wanted to understand if they may be responsible for PFAS contamination detected in a nearby town’s groundwater
MPCA, 2022

## Slide 7
PFAS groundwater data from each of the three sources was compared to the PFAS groundwater data from the Town
Historical research identified two other potential PFAS sources proximate to the Town
Which PFAS Source Impacted the Town’s Groundwater?

## Slide 8
Statistical Evaluation of PFAS Datasets
Principal Component Analysis (PCA)
A statistical technique used to project multi-dimensional data onto two
or three dimensions for visualization and possible source identification
Town Samples
Client Site Samples
Source B Samples
Source C Samples
Client’s
Site
Source
B
Source
C

## Slide 9
Groundwater Flow Patterns Support the Conclusion That Source C is the PFAS Contributor to the Town’s Groundwater
Client’s
Site
Source
B
Source
C
Local GW Flow Direction
PFAS compounds are soluble and travel with groundwater in the subsurface
Analysis of groundwater flow patterns revealed that groundwater beneath Source C flows directly under the town, while groundwater at the Client’s site and Source B flows toward the river downgradient of the town

## Slide 10
Historical research identified two additional potential PFAS sources proximate to the town
PFAS groundwater data from each of the three sites was compared to the town’s PFAS groundwater data using a robust statistical tool
An evaluation of the fate and transport of PFAS in groundwater in the area supported the conclusion that another source released the PFAS found in the town’s groundwater
Multiple LOEs Indicated That an Alternate Source was Responsible for PFAS Contamination in the Town’s Groundwater

## Slide 11
Case Study 2:
Petroleum Age Dating at an Underground Storage Tank Site

## Slide 12
Case Study 2 Background
The Case: A property owner sued its former fuel distributor for diesel contamination of soil and groundwater discovered in the 2010s
The client was contractually obligated to operate and maintain the underground fuel distribution system while the contract was in effect, but the contract expired in the 1980s
The date of release is of paramount importance, as releases following contract expiration are not the client’s responsibility
Source: https://www.greentraxinc.com/what-makes-my-underground-storage-tank-ust-commercial-vs-residential/

## Slide 13
What Happens Over Time After Petroleum is Released to the Environment?
Refined petroleum products contain thousands of unique compounds
  Each of these compounds weather at a different rate in the environment
If the starting composition is known, one can estimate the age of a petroleum release by assessing the relative abundance of “fast weathering” and “slow weathering” compounds
  Abundant “fast weathering” compounds = fresh release
  Depleted “fast weathering” compounds = older release
Petroleum weathering over time
Source: https://www.shine.cn/news/metro/2007222712/

## Slide 14
Lab Chromatogram Evaluation for Release Dating

## Slide 15
Quantitative Release Dating Using Ratios
Source: Christensen and Larsen, 1993.
Sample No. | N-C17 to Pristane Ratio | Age of Diesel Spill | Probable Release Date (samples collected in 2020)
1 | 0.80 | 13 years | ca. 2007
2 | 0.91 | 12 years | ca. 2008
3 | 1.15 | 10 years | ca. 2010
4 | 0.68 | 14 years | ca. 2006

## Slide 16
Multiple LOEs Indicated That the Client Was Not Responsible for the Diesel Contamination, as It Was Released Post-1980
Chromatogram patterns alongside quantitative aging estimates support a modern petroleum release
Client was not liable for environmental damages after their 1980 contract expiration

## Slide 17
Conclusions
A multiple LOE approach for environmental forensics can provide attorneys and their clients with defensible technical arguments in support of mediation & litigation proceedings under various regulatory frameworks
Forensic tools can be applied at a wide variety of sites impacted by a diverse suite of environmental contaminants (including both legacy and emerging contaminants)

## Slide 18
Questions?
Emmie Chen, P.E.
echen@geosyntec.com